## Slide 1
MACHINE LEARNING (25SC2107E)
Soft Actor-Critic Based Semantic-Aware Resource Allocation for Hybrid Semantic / Bit NOMA Networks
Deep reinforcement learning for power and time allocation in hybrid NOMA-OFDMA systems
N.Jesly Monica
Roll No.2520040052
M.Shreya
Roll No.2520040063
P.Karthika
Roll No.2520040094
Notes: Introduce the team and the project title. One line: we use Soft Actor-Critic reinforcement learning to decide how much transmit power and transmission time each user gets in a network that mixes semantic users and conventional bit users.

## Slide 2
Problem Statement
SAC · Semantic-Aware Hybrid NOMA | ML (25SC2107E) Review 2
Next-generation networks will serve two kinds of users at once: semantic users who care about the meaning of transmitted information, and conventional bit users who care about raw data rate. A base station must share one power budget and one frame of time among all of them.
OBJECTIVE
Learn a policy that maps channel and user state to per-user power and time allocation, jointly maximising throughput, semantic utility, QoS, fairness and energy efficiency.
Mixed traffic types
Equal or rate-only allocation ignores how important a semantic user's information is.
Scarce shared resources
One power budget, one frame duration and only a few OFDMA subcarriers for many users.
Dynamic and non-convex
Random fading and NOMA interference make per-frame optimisation hard to solve analytically.
Notes: Explain why this is hard: two user types with different goals, one shared power and time budget, and a channel that changes every frame. Classical optimisation would need to be re-solved every frame, so we learn a policy instead.

## Slide 3
System Model
SAC · Semantic-Aware Hybrid NOMA | ML (25SC2107E) Review 2
Chart: Simulated 100 m × 100 m cell (one realisation)
| 38.9 | 28.1 | 54.3 | 14.1 | 77.2 | 81.5 | 70.7 | 72.9 | 77.1 | 35.8 | 11.6 | 27.1 | 82.9 | 35.7 | 80.2 | 7.5 | 98.7 | 19.9 | 0.6 | 7.4 | 50
Semantic users | 86.3 | 31.1 | 32.5 | 73 | 12 | 56.1 | 77.1 | 49.4 | 52.3 | 2.5 | 10.8
Bit users | 62.3 | 33.1 | 6.4 | 63.8 | 88.7 | 47.2 | 71.3 | 76.1 | 42.8
Base station | 50
User inputs (defaults)
Number of users | 20 (11 semantic, 9 bit)
OFDMA subcarriers | 5 (4 users each)
Total bandwidth | 10 MHz (2 MHz / subcarrier)
BS power budget | 10 W
Frame duration | 1 s
Simulator assumptions
Carrier frequency | 2.4 GHz
Small-scale fading | Rayleigh
Path-loss exponent | 3.0
Noise density | 4 × 10⁻²¹ W/Hz
Per-user position, fading, semantic importance (0.4–1.0) and target rate (0.5–3 Mbps) are generated automatically each frame.
Notes: Only five values are user inputs. Everything else about each user, including location, channel gain, whether it is semantic or bit, its semantic importance and its target rate, is generated by the simulator. Roughly half the users are semantic.

## Slide 4
Hybrid NOMA-OFDMA Scheduling & Semantic Utility
SAC · Semantic-Aware Hybrid NOMA | ML (25SC2107E) Review 2
Sort users
by channel gain, weak → strong
›
OFDMA split
round-robin onto 5 orthogonal subcarriers
›
NOMA cluster
4 users share each subcarrier via SIC
›
Evaluate
SINR, rate and semantic utility per user
SINR (P_str = power of stronger users in the same cluster)
SINRᵤ = pᵤ gᵤ / ( gᵤ · P_str + σ² )
Achievable rate on subcarrier bandwidth B_sc
Rᵤ = B_sc · log₂(1 + SINRᵤ)
Semantic utility (importance-weighted delivered information)
U_sem = Σᵤ sᵤ · Rᵤ · τᵤ T
pᵤ: power · gᵤ: channel gain · τᵤ: time fraction · T: frame duration · sᵤ: semantic importance (0 for bit users)
Notes: The scheduler is deterministic: it groups users onto subcarriers so SAC only has to learn power and time. Within a subcarrier we use a simplified downlink NOMA model. Semantic utility is a proxy: semantic importance times delivered megabits. Bit users have importance zero, so they only count through throughput and QoS.

## Slide 5
Proposed Method: SAC Problem Formulation
SAC · Semantic-Aware Hybrid NOMA | ML (25SC2107E) Review 2
State
5 features × 20 users = 100
Normalised channel quality
Normalised distance
Semantic importance
Normalised target rate
Subcarrier index
Action
2 × 20 + 1 = 41 (continuous)
20 power logits → softmax split
20 time logits → softmax split
1 scalar → fraction of budget used (5–100%)
Reward
weighted multi-objective
Chart: 
| Throughput | Semantic | QoS | Fairness | Energy eff.
Weight | 30 | 30 | 15 | 15 | 10
r = 0.30·Throughput + 0.30·Semantic utility + 0.15·QoS + 0.15·Fairness + 0.10·Energy eff.
Softmax guarantees Σ power ≤ budget and Σ time = one frame, so every action is feasible by construction; one frame = one decision (episode).
Notes: The agent sees five features per user. Its action is 41 continuous numbers. Softmax turns the logits into valid fractions, so the constraints are always satisfied without penalty terms. The reward balances five objectives with fixed weights; semantic utility has the same weight as throughput.

## Slide 6
Soft Actor-Critic Agent
SAC · Semantic-Aware Hybrid NOMA | ML (25SC2107E) Review 2
Actor π(a|s)
Gaussian + tanh squash
Environment
Hybrid NOMA-OFDMA sim
Replay buffer
50,000 transitions
Twin critics Q₁, Q₂
+ target nets (τ = 0.005)
Automatic entropy tuning α
target entropy = −41 → keeps exploration alive
action
(s, a, r)
batch
min(Q₁,Q₂)
Hyperparameters
Hidden layers | 2 × 128, ReLU
Optimiser / LR | Adam, 3 × 10⁻⁴
Discount γ | 0.99
Soft update τ | 0.005
Batch size | 128
Training episodes | 1,200
Random warm-up | 300 episodes
Evaluation | 200 episodes
Why SAC: off-policy (sample-efficient), handles a 41-dim continuous action space, and entropy regularisation avoids premature collapse.
Notes: SAC is an off-policy actor-critic method. Two critics are trained and the minimum is used to avoid overestimation. The temperature alpha is learned automatically. We chose SAC over DQN because our action is continuous and 41-dimensional.

## Slide 7
Implementation Workflow
SAC · Semantic-Aware Hybrid NOMA | ML (25SC2107E) Review 2
1
Configure
Users, subcarriers, bandwidth, power, frame time
2
Generate
Positions, Rayleigh fading, semantic profile
3
Schedule
OFDMA subcarriers + NOMA clusters
4
Act
SAC outputs power & time allocation
5
Evaluate
Rate, semantic utility, QoS, EE → reward
6
Learn
Store in buffer, update actor & critics
↻ repeated for 1,200 episodes (each episode = new channel realisation)
Baseline
Equal allocation: every user gets P_max / N power and T / N time on the same scheduler, evaluated on 200 fresh channel realisations.
Tech stack
Python
PyTorch
NumPy
Pandas
Matplotlib
Jupyter
Notes: Walk through one loop: configure, generate a channel, schedule users onto subcarriers, SAC chooses power and time, the simulator computes metrics and reward, and the transition is stored and used to update the networks. The first 300 episodes use random actions to fill the buffer.

## Slide 8
Simulation Results
SAC · Semantic-Aware Hybrid NOMA | ML (25SC2107E) Review 2
Chart: SAC training reward (100-episode moving average)
| 100 | 125 | 150 | 175 | 200 | 225 | 250 | 275 | 300 | 325 | 350 | 375 | 400 | 425 | 450 | 475 | 500 | 525 | 550 | 575 | 600 | 625 | 650 | 675 | 700 | 725 | 750 | 775 | 800 | 825 | 850 | 875 | 900 | 925 | 950 | 975 | 1000 | 1025 | 1050 | 1075 | 1100 | 1125 | 1150 | 1175 | 1200 | 1200
Reward (100-episode moving avg.) | 0.5207 | 0.5265 | 0.5414 | 0.544 | 0.5407 | 0.5373 | 0.5248 | 0.5184 | 0.5307 | 0.525 | 0.5312 | 0.5296 | 0.5257 | 0.5385 | 0.5417 | 0.5375 | 0.5404 | 0.534 | 0.5167 | 0.5218 | 0.5205 | 0.5195 | 0.5231 | 0.5226 | 0.526 | 0.5396 | 0.546 | 0.5463 | 0.5358 | 0.5241 | 0.528 | 0.5251 | 0.5348 | 0.5315 | 0.5347 | 0.5321 | 0.528 | 0.5391 | 0.5323 | 0.5363 | 0.5371 | 0.5337 | 0.5432 | 0.5437 | 0.543 | 0.543
Chart: SAC vs equal allocation (% change, 200 test episodes)
| Energy efficiency | Reward | Fairness | Semantic utility | QoS | Throughput | Power used
% change | 85.9 | 0.9 | 0.5 | -0.4 | -0.5 | -3.4 | -48.1
Default configuration (20 users, 5 subcarriers, 10 MHz, 10 W, 1 s), seed 42. Replace with your own run's numbers if they differ.
Notes: Left: the training reward is noisy because every episode is a new random channel; the moving average ends slightly above where it started. Right: compared with equal allocation on 200 unseen channels, SAC nearly doubles energy efficiency and halves power, while throughput, semantic utility and QoS stay within a few percent.

## Slide 9
Key Findings
SAC · Semantic-Aware Hybrid NOMA | ML (25SC2107E) Review 2
+86%
Energy efficiency
3.05 vs 1.64 Mbps/W
−48%
Transmit power used
5.19 W vs 10 W
96.6%
Throughput retained
15.86 vs 16.42 Mbps
SAC learned budget control
NOMA clusters are interference-limited: scaling all powers down barely changes SINR, so SAC cuts total power to ~52% of the budget with almost no rate loss.
Per-user split is still near-uniform
Semantic users are not yet prioritised (semantic utility −0.4%). The reward signal is dominated by channel randomness, so fine-grained allocation has not emerged in 1,200 episodes.
Notes: Be honest about both results. The good news: SAC discovered that it can save about half the power and still deliver about the same throughput, which nearly doubles energy efficiency. The limitation: it has not yet learned to favour important semantic users; that is our main remaining work.

## Slide 10
Current Progress & Remaining Work
Completed
System model & channel simulator
Hybrid NOMA-OFDMA scheduler
SAC agent (actor, twin critics, auto-α)
Training + evaluation vs equal allocation
Remaining
Reward shaping to prioritise semantic users
Stronger baselines (DDPG / PPO, water-filling)
Multiple seeds; scaling with users & subcarriers
GitHub repo: docs, results & run instructions
Individual contributions
Member 1
System model, channel generation & NOMA-OFDMA scheduler
Member 2
SAC agent design, reward formulation & training
Member 3
Baseline, evaluation, result analysis & GitHub repo
github.com/<your-username>/<repo-name>
Notes: Each member presents their own part here. Contribution lines are suggestions; edit them to match who actually did what. Close by pointing to the GitHub repository.