## Slide 1
MACHINE LEARNING PROJECT (25SC2107E)
KL University
Soft Actor-Critic Based Semantic-Aware Resource Allocation for Hybrid NOMA Networks
Joint power and transmission time optimization using continuous deep reinforcement learning in dynamic OFDMA-NOMA wireless environments.
PROJECT TEAM
N. Jesly Monica (2520040052) | M. Shreya (2520040063) | P. Karthika (2520040094)
SUPERVISOR
Mr. N Lava Prasad (Assistant Professor, Dept. of ECE)

## Slide 2
Core Challenges
Problem Statement
Objective: Design an autonomous Soft Actor-Critic (SAC) DRL framework to optimize power and time allocation jointly for semantic utility, throughput, QoS, fairness, and energy efficiency.
Heterogeneous User Traffic
•
Semantic Users: Require high information importance ($s_u > 0$).
•
Conventional Bit Users: Require raw data transmission rate ($s_u = 0$).
•
Traditional schedulers treat all data bits equally.
NOMA Interference & Dynamic Channels
•
Intra-cluster Interference: Co-channel users share spectrum.
•
Fading Dynamic: Non-convex power control under Rayleigh fading.
•
Analytical optimization is computationally intractable per frame.
Resource Scarcity Trade-offs
•
Tight Budgets: $10\text{ W}$ transmit power, $1.0\text{ s}$ frame time window.
•
Multi-objective Conflict: Throughput vs fairness vs energy.
•
Need adaptive model for continuous allocation control.

## Slide 3
Parameter | Value / Specification
Active Users ($N$) | 20 heterogeneous users (50% Semantic / 50% Bit)
OFDMA Subcarriers ($K$) | 5 subcarriers ($2\text{ MHz}$ bandwidth per subcarrier)
Total Bandwidth ($B$) | $10.0\text{ MHz}$ total system bandwidth
BS Power Budget ($P_{\max}$) | $10.0\text{ W}$ base station transmit power limit
Frame Duration ($T$) | $1.0\text{ s}$ per transmission decision window
Channel Fading & Loss | Rayleigh fading, path loss exponent $\alpha = 3.0$
Physical Simulation Environment
System Architecture & Parameters
System Specifications
Semantic Users
Semantic Importance $s_u \in [0.4, 1.0]$. Utility evaluated by importance-weighted information delivery.
Conventional Bit Users
Semantic Importance $s_u = 0.0$. Transmission focus strictly on achieving target bit rate demand.
Target Rates & Distances
Target demand $R_u^{\text{target}} \in [0.5, 3.0]\text{ Mbps}$. Uniform spatial placement inside $100\text{m} \times 100\text{m}$ cell.

## Slide 4
Proposed Methodology
Hybrid NOMA-OFDMA & Semantic Utility Model
STAGE 1
OFDMA Subcarrier Pairing
STAGE 2
Downlink NOMA & SIC Interference
STAGE 3
Semantic Utility Formulation
USER DOWNLINK SINR
$\text{SINR}_u = \frac{p_u g_u}{\sum_{v > u} p_v g_u + \sigma^2}$
ACHIEVABLE BIT RATE
$R_u = B_{\text{sub}} \cdot \log_2(1 + \text{SINR}_u)$
SEMANTIC UTILITY PROXY
$U_{\text{sem}} = \sum_{u=1}^N s_u \cdot [R_u \cdot (t_u T)]$
•
Sort users by channel gain $g_u$ (weak to strong).
•
Distribute $N=20$ users across $K=5$ subcarriers.
•
4 users grouped per subcarrier.
•
Successive Interference Cancellation (SIC) applied.
•
Stronger users decode and cancel weaker signals.
•
SINR calculation includes residual co-subcarrier power.
•
Evaluates importance-weighted throughput.
•
Delivered Mbits: $D_u = R_u \cdot (t_u \cdot T)$.
•
Utility Proxy: $U_{\text{sem}} = \sum s_u \cdot D_u$.

## Slide 5
Reinforcement Learning Modeling
Soft Actor-Critic MDP Formulation
Normalized observations collected per frame:
Continuous control decision variables:
Multi-objective weighted function:
State Space $\mathcal{S}$ ($5N$ Dim)
•
Channel Quality ($g$): Normalized gain ratio.
•
Distance ($d$): Normalized user location.
•
Semantic Importance ($s$): User weight $s_u$.
•
Target Data Rate ($r$): Traffic demand.
•
Subcarrier Index ($sc$): Grouping ID.
Action Space $\mathcal{A}$ ($2N+1$ Dim)
•
Power Logits ($N$): Transmit power split.
•
Time Logits ($N$): Transmission time split.
•
Budget Scalar ($1$): Power usage level ($5\% \text{ to } 100\%$).
•
Softmax conversion guarantees valid budget splits.
Composite Reward $R$
•
$30\%$ Throughput: Total rate delivered.
•
$30\%$ Semantic Utility: $U_{\text{sem}}$ metric score.
•
$15\%$ QoS Satisfaction: Rate ratio achieved.
•
$15\%$ Fairness: Jain's index on rates.
•
$10\%$ Energy Efficiency: Mbps/Watt ratio.

## Slide 6
Algorithm Design
Soft Actor-Critic (SAC) Agent Architecture
SAC Objective Maximization: $J(\pi) = \sum_{t=0}^T \mathbb{E}_{(s_t, a_t)} \left[ r(s_t, a_t) + \alpha \mathcal{H}(\pi(\cdot|s_t)) \right]$
Neural Network Components
Hyperparameters & Training Setup
Gaussian Actor Network $\pi_\theta(a|s)$
Outputs Gaussian mean $\mu$ and std $\sigma$. Uses Tanh squashing to bound actions continuously in $[-1, 1]$.
Twin Critic Networks $Q_{\phi_1}(s,a), Q_{\phi_2}(s,a)$
Evaluates state-action pair values. Takes minimum output $\min(Q_1, Q_2)$ to prevent overestimation bias.
Automatic Entropy Temperature ($\alpha$)
Dynamically adjusts entropy temperature $\alpha$ to balance exploration vs exploitation during learning.
•
Network MLP Hidden Units: 2 hidden layers (128 units each, ReLU activation).
•
Optimizer & Learning Rate: Adam optimizer with $\text{lr} = 3 \times 10^{-4}$.
•
Discount & Soft Update: Gamma $\gamma = 0.99$, Polyak tau $\tau = 0.005$.
•
Replay Buffer & Batch: 50,000 transition capacity, batch size 128.
•
Training Schedule: 1,200 training episodes (300 warmup steps).

## Slide 7
Implementation Overview
Project Execution & Simulation Workflow
Software & Tools Stack:
Python 3.x | PyTorch | Gymnasium | NumPy | Pandas | Matplotlib | Google Colab
1
System Init
Configure users, bandwidth, and base station power budget.
2
Channel Sample
Simulate random user positions, Rayleigh fading & path loss.
3
NOMA Pairing
Group users onto subcarriers based on channel quality order.
4
SAC Decision
Actor policy outputs continuous power & time allocation.
5
SAC Update
Store transition in buffer and optimize Actor-Critic networks.

## Slide 8
Evaluation Metric | Equal Allocation | SAC Allocation | Performance Impact
Average System Reward | 0.3704 | 0.4357 | +17.6% Gain
Energy Efficiency (Mbps/W) | 1.642 Mbps/W | 3.054 Mbps/W | +86.0% Boost
Transmit Power Used (W) | 10.00 W (Full) | 5.19 W | -48.1% Power Saved
Throughput (Mbps) | 16.42 Mbps | 15.86 Mbps | Retains 96.6% Rate
QoS Satisfaction Ratio | 0.812 | 0.841 | +3.6% Improvement
Simulation Results
SAC vs Equal Allocation Baseline (200 Episodes)
Critical Finding
NOMA channels are interference-limited. SAC learned that blasting max power ($10\text{ W}$) adds excessive co-channel interference. Reducing power to $5.19\text{ W}$ doubles energy efficiency while maintaining full user rate.
Dynamic Convergence
SAC converges smoothly within ~400 episodes, maintaining training stability via entropy maximization and twin critic minimization.

## Slide 9
Experimental Output Visualization
Colab Simulation Output Plots & Line Analysis
SAC TRAINING COMPLETE
Final Episode Log: Reward: 1.0321 | Throughput: 17.889 Mbps | Semantic Utility: 5.504 | QoS: 0.748 | Alpha: 0.7247
Plot Analysis: Illustrates random spatial distribution of $N=10$ active users ($\bullet$) around the central Base Station ($\mathbf{\Delta}$) located at $(50,50)$, demonstrating varying Rayleigh path-loss profiles across the cellular area.
Plot Analysis: Shows initial exploration fluctuations giving way to a steady reward convergence around $\sim 1.12$ (50-episode moving average line), confirming stable policy optimization without gradient degradation.
Plot Analysis: Tracks continuous total throughput maintaining high performance levels between $19\text{--}21\text{ Mbps}$ across 1200 episodes, proving power efficiency cuts do not compromise overall network throughput capacity.
1. Simulated User Positions
2. SAC Training Reward Curve
3. Throughput During Training

## Slide 10
Project Deliverables & Team Work
Limitations & Future Scope
INDIVIDUAL CONTRIBUTIONS
Completed
•
System model & channel simulator
•
Hybrid NOMA-OFDMA scheduler
•
SAC agent (actor, twin critics, auto-$\alpha$)
•
Training + evaluation vs equal allocation
Remaining
•
Reward shaping to prioritise semantic users
•
Stronger baselines (DDPG / PPO, water-filling)
•
Multiple seeds; scaling with users & subcarriers
•
GitHub repo: docs, results & run instructions
Member 1
System model, channel generation & NOMA-OFDMA scheduler & GitHub repo
Member 2
SAC agent design, reward formulation & training Baseline, evaluation,
Member 3
result analysis , Literature survey , Project Report.